## Slide 1: Memory Organization
Memory Hierarchy
  Memory hierarchy in a computer system :
    Main Memory : memory unit that communicates directly with the CPU (RAM)
    Auxiliary Memory : device that provide backup storage (Disk Drives)
    Cache Memory : special very-high-speed memory to increase the processing speed (Cache RAM)

## Slide 2: Memory Organization
  Multiprogramming
    enable the CPU to process a number of independent program concurrently
  Memory Management System :
    supervise the flow of information between auxiliary memory and main memory
Memory Hierarchy is to obtain the highest possible access speed while minimizing the total cost of the memory system
Register
Cache
Main Memory
Magnetic Disk
Magnetic Tape

## Slide 3: Random Access Memory (RAM)
  RAM Chips
  Static RAM
  Consists of Flip-flops to store binary information.
  Static RAM is easier to use and having short Read/Write cycles
  Used mostly in Cache memory.
  Dynamic RAM
  Stores binary information in the form of electric charge stored inside the capacitor.
  The capacitors are provided by MOS transistors.
  Refreshing circuit is required to refresh the memory.
  Dynamic RAM offers reduced power consumption and large storage capacity.
  It is used to construct main memory.
    Typical RAM chip :
      128 X 8 RAM : 27 = 128 (7 bit address lines)
    Typical ROM chip:
      512 X 8 ROM : 29 = 512 (9 bit address lines

## Slide 4: MAIN MEMORY
RAM and ROM Chips
Typical RAM chip
Typical ROM chip
Chip select 1
Chip select 2
Read
Write
7-bit address
CS1
CS2
RD
WR
AD 7
128 x 8
RAM
8-bit data bus
CS1 CS2 RD WR
0 0 x x
0 1 x x
1 0 0 0
1 0 0 1
1 0 1 x
1 1 x x
Memory function
Inhibit
Inhibit
Inhibit
Write
Read
Inhibit
State of data bus
High-impedence
High-impedence
High-impedence
Input data to RAM
Output data from RAM
High-impedence
Chip select 1
Chip select 2
9-bit address
CS1
CS2
AD 9
512 x 8
ROM
8-bit data bus
Main Memory

## Slide 5: MEMORY ADDRESS MAP
RAM 1
RAM 2
RAM 3
RAM 4
ROM
0000 - 007F
0080 - 00FF
0100 - 017F
0180 - 01FF
0200 - 03FF
Component
Hexadecimal
address
0 0 0 x x x x x x x
0 0 1 x x x x x x x
0 1 0 x x x x x x x
0 1 1 x x x x x x x
1 x x x x x x x x x
10 9 8 7 6 5 4 3 2 1
Address bus
Memory Connection to CPU
- RAM and ROM chips are connected to a CPU
through the data and address buses
- The low-order lines in the address bus select
the byte within the chips and other lines in the
address bus select a particular chip through
its chip select inputs
Address space assignment to each memory chip
Example: 512 bytes RAM and 512 bytes ROM
Main Memory

## Slide 6: CONNECTION OF MEMORY TO CPU
Main Memory
CS1
CS2
RD
WR
AD7
128 x 8
RAM 1
CS1
CS2
RD
WR
AD7
128 x 8
RAM 2
CS1
CS2
RD
WR
AD7
128 x 8
RAM 3
CS1
CS2
RD
WR
AD7
128 x 8
RAM 4
Decoder
3
2
1
0
WR
RD
9
8
7-1
10
16-11
Address bus
Data bus
CPU
CS1
CS2
512 x 8
ROM
AD9
1- 7
9
8
Data
Data
Data
Data
Data

## Slide 7: Numerical Problems
Q1. a) How many 128x8 RAM chips are needed to provide a memory capacity of 2048 bytes.
b) How many lines of the address bus must be used to access 2048 bytes of memory. How many of these lines will be common to all chips.
c) How many lines must be decoded for chip select? Specify the size of decoders.
Q2. Extend the memory system of Fig.1 to 4096 bytes of RAM. List the memory-address map and indicate what size decoders are needed.
Q3. A computer employs RAM chips of 256x8 and ROM chips of 1024x8. The computer system needs 2K bytes of RAM, 4K bytes of ROM, and four interface units each with four registers. A memory-mapped I/O configuration used. The two highest-order bits of the address bus are assigned 00 for RAM, 01 for ROM, and 10 for interface registers.
How many RAM and ROM chips are needed.
Draw a memory-address map for the system.
Give the address range in hexadecimal for RAM, ROM and interface.

## Slide 10: Cache Memory
12-5 Cache Memory
  Locality of Reference
    the references to memory tend to be confined within a few localized areas in memory
  Cache Memory : a fast small memory
    keeping the most frequently accessed instructions and data in the fast cache memory
  Hit Ratio
    the ratio of the number of hits divided by the total CPU references (hits + misses) to memory
      hit : the CPU finds the word in the cache
      miss : the word is not found in cache (CPU must read main memory)
  A computer with cache access time of 100ns, a main memory access time of 1000 ns, a hit ratio of 0.9 is having average access time of 200ns.

## Slide 11: Types of Mapping of Cache Memory
  Mapping
    The transformation of data from main memory to cache memory
      1) Associative mapping
      2) Direct mapping
      3) Set-associative mapping
  Associative Mapping:
    main memory : 32 K x 12 bit word (15 bit address lines)
    cache memory : 512 x 12 bit word
      CPU sends a 15-bit address to cache
        Hit : CPU accepts the 12-bit data from cache
        Miss : CPU reads the data from main memory (then data is written to cache)

## Slide 12: Associative Mapping

## Slide 13: Direct Mapping
  Direct mapping :
    n bit memory address
    Tag field (n - k) : Index field (k)
    2k words cache memory + 2n words main memory
        Tag = 6 bit (15 - 9), Index = 9 bit

## Slide 14: Direct Mapping
    Direct mapping cache with block size of 8 words :
      64 block x 8 word = 512 cache words size

## Slide 15: Set-Associative Mapping
  Set-associative mapping : (two-way)

## Slide 16: Questions
A two-way set associative cache memory uses blocks of four words. The cache can accommodate a total of 2048 words from main memory. The main memory size is 128Kx32. Formulate all pertinent information required to construct the cache memory. What is the size of cache memory.
The access time of a cache memory is 100ns and that of main memory is 1000ns. It is estimated that 80 percent of the memory requests are for read and the remaining 20 percent for write. The hit ratio for read access only is 0.9. A write-through procedure is used. What is the average access time of the system considering only memory read cycles. What is the average access time of the system for both read and write requests. What is the hit ratio considering the write requests also
A computer has a memory unit of 64Kx16 and a cache memory of 1K words. The cache uses direct mapping with a block size of four words. How many bits are there in the tag, index, block, and words fields of the address format. How many bits are there in each word of cache, and how are they divided into functions? Include a valid bit. How many blocks can the cache accommodate?

## Slide 17: Answer

## Slide 18: Answer

## Slide 19
  Replacement Algorithm : cache miss or full
    1) LRU (Least Recently Used):
    2) Random Replacement:
    3) FIFO (First-In First-Out) :
  Writing to Cache :
      1) Write-through : Every operation result write into cache as well as main memory.
      2) Write-back : After every operation cache result will update, only final result need to copy into main memory.
  Cache Initialization
    Cache is initialized :
      1) When power is applied to the computer
      2) When main memory is loaded with a complete set of programs from auxiliary memory
      3) Cache is initialized by clearing all the valid bits to 0.
    Valid bit
      Indicate whether or not the word contains valid data

## Slide 20
VIRTUAL MEMORY
Give the programmer the illusion that the system has a very large memory,
even though the computer actually has a relatively small main memory
Address Space(Logical) and Memory Space(Physical)
virtual address
(logical address)
physical address
address space
memory space
address generated by programs actual main memory address
Mapping
Virtual Memory

## Slide 21: PAGE REPLACEMENT ALGORITHMS
FIFO
0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
7
0
1
0
0
7
1
2
0
1
2
3
1
2
3
0
4
3
0
4
2
0
4
2
3
0
2
3
0
1
3
0
1
2
7
1
2
7
0
2
7
0
1
Page frames
Reference string
FIFO algorithm selects the page that has been in memory the longest time
Optimal Replacement (OPT) - Lowest page fault rate of all algorithms
Replace that page which will not be used for the longest period of time
0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
7
0
1
0
0
7
1
2
0
1
2
0
3
2
4
3
2
0
3
2
0
1
7
0
1
Page frames
Reference string
Virtual Memory

## Slide 22: PAGE REPLACEMENT ALGORITHMS
- OPT is difficult to implement since it requires future knowledge
Replace that page which has not been
used for the longest period of time
LRU (Least Recently Used)
0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
7
0
1
0
0
7
1
2
0
1
2
0
3
4
0
3
4
0
2
4
3
2
0
3
2
1
3
2
1
0
2
1
0
7
Page frames
Reference string
Virtual Memory

## Slide 23: Question
The page request are in following order. If there are three memory frames, show the execution of the following pages using
a. FIFO b. Optimal c. LRU
6 0 1 3 2 5 0 4 7 1 3 2 6 0 4

## Slide 24: Input-Output Organization
Peripheral Devices: Input & Output devices attached to computer are called Peripheral.
Input and output devices communicate alphanumeric information by using ASCII 7bit code.
To use computer efficiently, large number of programs and data must be prepared in advance for execution with computer.
I/O interface provides a method for transferring information between internal storage and external I/O devices.
    .

## Slide 25: Input-Output Interface
The purpose of interfacing are as follows:
  Peripherals are electromechanical & electromagnetic devices and are interacting with electronics devices(CPU).
  Data transfer rate of peripherals is usually slower than transfer rate of CPU.
  Data codes and formats in peripherals differ from word format in CPU
  Operating modes of peripherals are different from each other and each one must be controlled without disturbing other.

## Slide 26: Input-Output Interface
To resolve these differences, computer system includes Interface units between CPU and peripherals to supervise and synchronize all input and output transfers.
Each peripheral has its own controller that operates a particular electromechanical device.
To communicate with a particular device, the processor places a device address on the address lines.

## Slide 27: Input-Output Interface

## Slide 28: Input-Output Interface
When the interface detects it own address, it activates path between bus lines and the device.
At the time address is made available in address lines, the processor provides function code(I/O command) in the control lines.
Types of I/O command:
Control command: To activate and inform what to do.
Status command: To test various status conditions.
Data Output data: It causes the transfer of data from bus into one of its registers.
Data Input Command: Interface receives data from peripheral and places them on buffer register where it is put into data lines.

## Slide 29: I/O versus Memory Bus
In addition to communicating to I/O, processor must also communicate with memory unit.
There are three ways that computer buses can be used to communicate with memory and I/O:
  Use two separate buses, one for memory and one for I/O. (IOP)
  Use one common bus for both memory and I/O but have separate control lines for each. (Isolated I/O)
  Use one common bus for memory and I/O with common control lines. (Memory Mapped I/O)

## Slide 30: Input-Output Transfer (IOP)
An IOP takes care of input and output tasks.
The CPU is assigned the task of initiating all operations, but I/O instructions are executed in IOP.
When an I/O operation is required, the CPU informs the IOP where to find the I/O program and then leaves the transfer details to the IOP.
IOP is also responsible of taking care of data synchronization, formats etc between CPU and I/O devices. In most computers CPU is master and IOP is slave.

## Slide 31: Input-Output Transfer (IOP)

## Slide 32: Isolated I/O
The distinction between memory and I/O transfer is made through separate read and control lines.
I/O read and I/O write are enabled during I/O transfer and Memory read/write are enabled during memory transfer.
In the isolated I/O configuration, CPU have distinct input and output instructions where each of it will be associated with address of the interface register.
When the CPU fetches and decodes the I/O instruction, it places the address associated with the instruction on the common address lines and enables I/O read or I/O write control line.

## Slide 33: Isolated I/O
When the CPU fetches and decodes the Memory instruction, it places the address associated with the instruction on the common address lines and enables Memory read or Memory write control line.
The isolated I/O method isolates memory and I/O addresses.

## Slide 34: Memory Mapped I/O
In this configuration, same address space is used for both memory and I/O.
The computer treats interface register (I/O) as a part of memory system.
The assigned address cannot be used for storing memory words, which reduces memory address range available.
In a memory-mapped I/O organization, there are no specific, input or output instruction.

## Slide 35: Memory Mapped I/O

## Slide 36: Modes of Transfer
Data transfer between the CPU and the I/O devices may be handled in variety of modes. Some modes use the CPU as an intermediate path and others transfer the data directly to and from the memory unit.
Data transfer to and from peripherals may be handled in three ways:
  Programmed I/O
  Interrupt-initiated I/O
  Direct Memory Access (DMA)

## Slide 37: Programmed I/O
Programmed I/O operations are the result of I/O instructions. Each data item transfer is initiate by an instruction in the program.
Usually the transfer is to and from a CPU register and peripheral. Other instructions are needed to transfer data between memory and CPU.
Once a data transfer is initiated, the CPU is required to monitor the interface to see when a transfer can again be made.

## Slide 38: Programmed I/O

## Slide 39: Interrupt Initiated I/O
In the programmed I/O CPU stays in program loop until the I/O indicates that it is ready for data transfer.
This is time consuming process since it makes CPU busy needlessly.
This can be avoided by using an interrupt facility.
When the interface determines that device is ready for data transfer, it generates an interrupt request.
Upon detecting external interrupt signal, the CPU momentarily stops the task it is processing.
It then branches to fulfill the I/O request and return to the original task.

## Slide 40: Direct Memory Access (DMA)
The transfer of data between a fast storage device such as magnetic disk and memory often limited to the speed of CPU.
Removing the CPU and letting the peripheral device manage the memory bus directly improve speed of transfer.
Such transfer technique is called Direct Memory Access (DMA).
A DMA controller takes over the buses to manage the transfer directly between I/O device and memory.
During DMA transfer, the CPU is idle and has no control over memory buses.
By using Bus Request(BR) and Bus Grant(BG) the buses are released to DMA controller.

## Slide 41: DMA
Data transfer ways:
  Burst Transfer: Here number of words are transferred in a block. Example: Magnetic disk.
  Cycle stealing: Allows the DMA controller to transfer one data word at a time after it must return the control of buses to CPU.

## Slide 42: DMA Controller

## Slide 43: Initialization of DMA
The CPU initializes the DMA by sending the following information through the data bus.
  The starting address of the memory block where data are available(for read) or where data are to be stored(for write).
  The word count, which is the number of words in the memory block.
  Control to specify the mode of transfer such as read or write.
  A control to start the DMA transfer.

## Slide 44: DMA Transfer in a computer system

## Slide 45: Bus Arbitration
The device that is allowed to initiate data transfers on the bus at any given time is called Bus master.
Bus arbitration is the process by which the next device becomes Bus master and will do the data transfer.
Two approaches: Centralized Arbitration and Distributed Arbitration.
        Centralized Arbitration

## Slide 46: Types of Interrupt
Major types of Interrupt are:
  External Interrupt: It comes from I/O devices, from timing device, or from any other external source.
  Internal Interrupt: It includes register overflow, invalid operation code, stack overflow etc.
  Software Interrupt or Hardware Interrupt: External and Internal interrupts are initiated from signals that occur in the hardware of the CPU. A software interrupt is initiated by executing an instruction.
  Priority Interrupt: In case several sources will request service simultaneously, in this case system must decide which device to service first. For ex: Polling, Daisy Chain (Priority chain).

## Slide 47: Buses
Data Bus: Bi-directional and transfers data.
Address Bus: Uni-directional and sends the address.
Control Bus: R/W, BR,BG etc.
Bus Structure: Single bus

## Slide 48: Buses
Bus Structure: Multi bus

## Slide 49: Synchronous or Asynchronous Data Transfer
Internal operations in a digital system are synchronized by means of clock pulses supplied by common pulse generator.
If the registers in the interface share a common clock with the CPU registers, the transfer is synchronous.
Asynchronous data transfer requires that control signals be transmitted between communicating units to indicate the time at which data is being transmitted.
Asynchronous data transfer can be accomplished by Strobe & Handshaking.

## Slide 50: Strobe Control
Strobe control:
  It employs single control line.
  It can be activated either by source or destination unit.

## Slide 51: Handshaking